## Slide 1: Lunch & Learn University of Calgary Schulich School of Engineering
HydroVault & Growth at TransAlta
April 17, 2024

## Slide 2: Agenda
Project Background
Proposed Reservoir Designs
Data Sources
Water Balance + Evaporation and Seepage
Hydrological Modelling & Analysis
Climate Scenarios & Future Storage
Operations Plan

## Slide 3: Project Background

## Slide 4: Background – Site Location
(Evolve Power, Tent Mountain Pumped Hydro Energy Storage 2023 https://evolvepower.ca/portfolio/tent-mountain-pumped-hydro-energy-storage/)
`

## Slide 5: The Pumped Hydro Energy Storage Concept
(Evolve Power, Tent Mountain Pumped Hydro Energy Storage 2023 https://evolvepower.ca/portfolio/tent-mountain-pumped-hydro-energy-storage/)
FUTURE WIND POWER DEVELOPMENT

## Slide 6: Scope of Work
Fall:
Upper Reservoir Design
Lower Reservoir Design
Winter:
Water Balance
Hydrological Modelling
Long-Term Climate Change Modelling
Operations Plan
Mitigation and Adaptation
(Evolve Power, Tent Mountain Pumped Hydro Energy Storage 2023 https://evolvepower.ca/portfolio/tent-mountain-pumped-hydro-energy-storage/)

## Slide 7: Proposed Reservoir Designs
These designs are the basis for our site analysis.

## Slide 8: Upper Reservoir
Water Level / Intake Level Selection
Option | Intake Level (MASL*) | Water Level (MASL*)
Lowest | 1760 | 1803
Medium | 1770 | 1807
Highest | 1777 | 1810
*Meters Above Sea Level
Lowest Option
Pros:
  Less grouting required
  Minimizes Dead Storage
  Least Expensive
Cons:
  Difficult Intake constructability

## Slide 9: Upper Reservoir
Legend
Blue Shade: Maximum Operating Water level.
Blue Line: Surface Grout Required.
Red Line: Vertical Seepage Cutoff Wall Required.
Purple Shade: No Seepage Reduction Required.
Water Level & Intake Level Explanation
Hatch, "Montem Resources Tent Mountain PSP Prefeasibility: Hydrological Assessment," TransAlta, 2022. [Online].

## Slide 10: Upper Reservoir
Vertical cut-off wall for the waste dump pile
  Slurry Walls
  Sheet pile/Geomembrane Walls
  Grouted Barrier Walls
Exterior grouting: Grouting methods to deal with cracks in non-waste material
  Consolidation Grouting
  Curtain Grouting
Grouting Requirements
Retained Water
Permeable Rock
Cut-off Wall

## Slide 11: Lower Reservoir
Water Level / Dam Placement
North Dam Location Alternatives
Alberta/BC Border
Lower Reservoir
Upper Reservoir
1
2
3
Alternative 3 North Dam
Pros:
  Least Inundated Crown Land Area
  Reduced Environmental Impact
  Lower Dead Storage Volume
  Cons:
  Smaller Catchment Area
  Require larger Dams

## Slide 12: Upper & Lower Reservoir Summary
Upper Reservoir
1803m
Lower Reservoir
1509m
Alberta/BC border
Dam Locations
Intake
El. 1760m
Dam | Crest Elevation (MASL*) | CDA Classification
South Dam | 1513 | Extreme
North Dam | 1512.5 | Extreme

## Slide 13: Data Sources
Challenges with meteorological and gauge data
EMDNA

## Slide 14: Challenges: Meteorological Data

## Slide 15: Challenges: Hydrometric Data (Gauge)

## Slide 16: Solution: EMDNA Dataset

## Slide 17: Water Balance
With specific emphasis on evapotranspiration and seepage.

## Slide 18: Tent Mountain Catchment Area Water Balance
Water Balance
Precipitation (P)
Groundwater Seepage (GW)
Evapo-transpiration (ET)
Runoff (R)
Change in Reservoir Storage (ΔS)
P-ET-∆S-GW=R
QR is the flow between reservoirs

## Slide 19: Precipitation & Evapotranspiration
Evapotranspiration
Transpiration
Evaporation
Precipitation

## Slide 20: Precipitation & Evapotranspiration
Precipitation
  EMDNA
  Averaged over 1979-2014
Evapotranspiration
  Modified Penman Equation using a weighted albedo for the basin
1979
2014

## Slide 21: Precipitation & Evapotranspiration
Annual Mean Precipitation = 1,149 mm
Annual Mean Evapotranspiration
= 861.5 mm

## Slide 22: Groundwater Seepage
E-W Cross-Section

## Slide 23: Groundwater Seepage
N-S Cross-Section

## Slide 24: Groundwater Seepage
N-S Flux (m3/s/m2) | E-W Flux (m3/s/m2) | Average Flux (m3/s/m2) | Wall Surface Area (km2) | Total Flux (m3/s)
1.63E-08 | 2.26E-10 | 8.26E-09 | 1.38E-01 | 1.14E-03
Annual Mean Groundwater Seepage = 7.95 mm
Seepage

## Slide 25: Change in Reservoir Storage
Annual Mean Change in Reservoir Storage = 1.9 mm
The graph depicts the simulated historical reservoir storage.

## Slide 26: Summary
P-ET-∆S-GW=R
1149 mm – 861 mm – 1.9 mm – 7.95 mm = 278 mm/year = 0.05 cms
Tributary of Crowsnest Creek flowing out of Tent Mountain site

## Slide 27: Hydrological Modelling
Hatch’s original model adapted to the purposes of (1) continuous simulation for climate modelling, and (2) event-based simulation for PMF simulation.

## Slide 28: Hydrological Model Workflow
Obtain original model from Hatch.
HEC-HMS
Continuous simulation for the Upper Reservoir.
Analysis and operation.
Future forcing data
Climate change impact assessment, PMF analysis.
Verify model setup and modify as necessary.
Structure, parameters
Ensure compatibility with intended purpose.
Validate modified model setup.
Historical forcing data
Ensure that simulated streamflow is realistic.

## Slide 29: Original Model Setup
Forcing data – daily surrogate observed temperature and precipitation
Catchment area – 1.356 km2
Calibration – 2018-2020 open water season water level
Evapotranspiration – ~750 mm/year
Seepage – summer 0.006 cms, winter 0.012 cms
Snow method – temperature index
Loss method – soil moisture accounting
Transform method – SCS UH, 39 min lag time
Model Schematic

## Slide 30: Adapted Model Setup – Continuous Simulation
Forcing data – daily EMDNA pseudo-observed temperature and precipitation
Catchment area – 1.311 km2 (Upper) & 4.246 km2 (Lower)
Calibration – assumed calibrated parameters valid
Evapotranspiration – modified Penman, 861 mm/year
Seepage – constant 0.0014 cms (Upper)
Snow & Loss methods – no change
Transform method – SCS UH, 39 min lag time (Upper), 60 min lag time (Lower)
+
Catchments modelled separately due to HEC-HMS routing limitations
Model Schematic

## Slide 31: Adapted Model Setup – Event-Based Simulation
Forcing data – synthetic SCS Type II storm (24-hour PMP of 247 mm), 5 min time step
Catchment area – no change
Calibration – assumed calibrated parameters valid
Evapotranspiration – none
Seepage – none
Snow method – no change
Loss method – no change
Transform method – no change
Catchments modelled together due to assumption of no pumping
Model Schematic

## Slide 32: Climate Modelling
Coupled Model Intercomparison Project Phase 6 (CMIP6)
Climate Change Projections

## Slide 33: Future Climate Projections
CMIP6 Model
Future Climate Scenarios
Scenario 1
Scenario 2
Scenario 3
Scenario 4
Positive human development
Society prioritizes economic and institutional growth
Sustainable practices
Renewable energies
Radiative forcing 2.6 Wm-2
Least impactful scenario
Society maintains current trends
Adoption of sustainable technology
Economic development at historical rates
Radiative forcing 4.5 Wm-2
Most realistic scenario
Pessimistic human development
Rapid population growth
Low education rate
Severe inequality
Prioritizing security
Radiative forcing 7.0 Wm-2
Second most impactful scenario
Rapid economic growth
Institutional improvement
Energy intensive projects
Increasing fossil fuel development
Radiative forcing 8.5 Wm-2
Most impactful scenario
Years 2015-2100

## Slide 34: Workflow
EMDNA Gridded data
Evaporation Calculation
Outflow
HEC-HMS
Hydro-Model
Historical
CMIP6 Model
Future Climate Scenarios
Scenario 1
Scenario 2
Scenario 3
Scenario 4
HEC-HMS
Hydro-Model
HEC-HMS
Hydro-Model
HEC-HMS
Hydro-Model
HEC-HMS
Hydro-Model
Future
S1 Outflow
S2 Outflow
S3 Outflow
S4 Outflow
Evaporation Calculation

## Slide 35: Climate Projection Results - Temperature
Historical Temperature Data
Scenario 2 Temperature Data
Average temperature ranges from -9 °C in December to 14 °C in July
Maximum temperature was 22 °C in July, minimum was -33 °C in February
Overall mean temperature appears to be around 3 °C
Average temperature ranges from -6 °C in December to 15 °C in July
Maximum temperature was 29 °C in July, minimum was -37 °C in February
Overall mean temperature appears to be around 6°C

## Slide 36: Climate Projection Results – Temperature
Average temperature increased by approximately 2 °C from historical to Scenario 1
Each climate scenario projects an additional 1 °C temperature increase
Scenario 4 predicts an average temperature of 5 °C higher than the historical temperature for Tent Mountain
Temperature variability is larger for more extreme climate scenarios
Temperature Scenario Comparison

## Slide 37: Climate Projection Results - Precipitation
Historical Precipitation Data
Scenario 2 Precipitation Data
Average precipitation per day ranges from 5 mm in June to 2.5 mm in July
The maximum daily precipitation event was 75 mm in June and September
Average projected precipitation per day ranges from 5 mm in November to 2 mm in July
The maximum projected daily precipitation event was 110 mm in July

## Slide 38: Climate Projection Results - Precipitation
Precipitation Scenario Comparison - Boxplot
Cumulative Average Monthly Precipitation
Median daily precipitation increases slightly as climate scenarios become more extreme
Summer months have median precipitations of zero in the climate projections
The highest projected cumulative monthly precipitation is around 140 mm in June, the lowest is around 60 mm in July
As climate change scenarios become more extreme more precipitation is expected at Tent Mountain

## Slide 39: Climate Projection Results - Storage
Scenario 2 Storage Results
Average Monthly Storage Results
The HEC model had storage full for both reservoirs, so adjustments had to be made to get the mean live storage to the 16-hour operational value of 7,107,000 m3
Maximum projected storage was 7,139,000 m3, minimum was 7,097,000 m3
The more extreme climate scenarios project less fluctuation in storage for the TM-PHES
Storage values are expected to be the highest in April and May, and the lowest in December and January

## Slide 40: Climate Projection Results - Storage
Storage Fluctuation Summary
Situation | Scenario | Volume (m3) | Operational Time (h) | Δ Upper Reservoir Water Level (mm)
Overall Max. | S2 | 7,139,000 | 16.07 | 116.03
Highest Max. Mean | S1 | 7,112,000 | 16.01 | 18.3
Lowest Max. Mean | S1 | 7,104,000 | 15.99 | -10.88
Overall Min. | S2 | 7,097,000 | 15.97 | -32.26

## Slide 41: Climate Projection Results - Outflow
Historical Outflow Results
Scenario 2 Outflow Results
Average daily outflow rate ranges from 0.5 m3/s in May to near 0 m3/s from July to March
Maximum outflow was 4.25 m3/s and occurred in May
Average daily outflow rate ranges from 0.2 m3/s in April and May to near 0 m3/s from July to January
Extreme outflow events are projected to occur in May and July, with a projected maximum value of 5.5 m3/s

## Slide 42: Climate Projection Results – Outflow
The biggest outflow outliers are projected to occur in Scenario 2
May and July are projected to have the biggest outliers, while outliers over 3 m3/s are common for all climate scenarios from March to June
Historical data has a large IQR in May, likely due to snowmelt runoff in this month
The largest projected outflow (which occurred in Scenario 2) is 30% larger than the largest historical outflow event
Outflow Scenario Outlier Comparison

## Slide 43: Climate Projection Results – PMP Estimate
PMP estimates from several sources for similar basins are between 200-300 mm.
PMP AEP on the eastern slopes of the Rockies estimated at 10-8.
Equivalent estimate based on:
  Historical: 125 mm.
  CMIP6 Scenario 2: 255 mm.
Historical record alone is insufficient for robust PMP estimation.
247 mm selected as PMP (mean of published range excluding outliers).
Tent Mountain
(approx.)
British Columbia Ministry of Environment and Climate Change Strategy, "Bulletin 2020-3-PMP, British Columbia Extreme Flood Project Probable Maximum Precipitation Guidelines – Technical Report."

## Slide 44: Climate Projection Results – PMF Estimate
247 mm PMP simulated using SCS type II hyetograph.
Governing scenario involves initially full Lower Reservoir.
15 m broad-crested spillway accomplishes 75% attenuation of PMF (130.4 cms inflow, 29.6 cms outflow).

## Slide 45: Operations Plan

## Slide 46: Operations Plan
Bridging the supply gaps in renewable energy generation

## Slide 47: Operations Plan
Historical AESO wind and solar generation data (2023) correlated to pool price data to identify trends and optimal times to pump
Potential for use of forecasted renewable generation data to identify optimized operational schedule for generation/pumping

## Slide 48: Operations Plan –Most Profitable Pool Price Hours Alberta 2022
Rank | 2022 Pool Price Hours in Alberta | Average Daily Pool Price ($/MWh)
1 | 5pm - 6pm | 292.83
2 | 6pm - 7pm | 260.88
3 | 4pm - 5pm | 256.05
4 | 7pm - 8pm | 246.58
5 | 8pm - 9pm | 220.42
6 | 3pm - 4pm | 211.85
7 | 2pm - 3pm | 190.44
8 | 1pm - 2pm | 188.39
9 | noon - 1pm | 176.48
10 | 9pm - 10pm | 170.75
11 | 11am - noon | 169.81
12 | 8am - 9am | 150.38
13 | 6am - 7am | 145.41
14 | 10am - 11am | 145.29
15 | 7am - 8am | 145.01
16 | 9am - 10am | 132.48
17 | 11pm - midnight | 131.94
18 | 10pm - 11pm | 116.37
19 | 5am - 6am | 103.98
20 | midnight - 1am | 95.21
21 | 1am - 2am | 91.24
22 | 2am - 3am | 87
23 | 4am - 5am | 85.59
24 | 3am - 4am | 84.91

## Slide 49: Operations Plan – Net Revenue for different pumping operations (4:5 generating to pumping)
Options (generating - pumping) | Net Revenue ($) | Annual percent difference between generating and pumping pool prices (%)
Max Option 1 (10.66-13.33) | 102,427,340.48 | 19.15
Set Option 1 (10.66-13.33) | 61,563,407.47 | 10.24
Max Option 2 (8-10) | 154,697,133.12 | 29.28
Set Option 2 (8-10) | 69,986,023.06 | 12.03
Max Option 3 (6-7.5) | 140,851,346.39 | 27.09
Set Option3 (6-7.5) | 73,131,677,06 | 12.79

## Slide 50: Operations Plan – Monthly % Differences Between Pumping and Generating Pool Prices
Max Option 1 |  | Set Option 1 |  | Max Option 2 |  | Set Option 2 |  | Max Option 3 |  | Set Option 3 | 
Month | % Difference | Month | % Difference | Month | % Difference | Month | % Difference | Month | % Difference | Month | % Difference
AUG | 37.67 | AUG | 44.57 | AUG | 52.06 | AUG | 39.16 | AUG | 44.62 | AUG | 31.06
DEC | 30.77 | SEP | 28.17 | SEP | 45.31 | JUL | 26.28 | SEP | 40.78 | SEP | 23.02
NOV | 26.97 | JUL | 27.39 | JUL | 33.84 | SEP | 25.14 | OCT | 31.91 | JUL | 22.85
SEP | 26.63 | JUN | 12.04 | OCT | 33.80 | JUN | 12.93 | JUL | 31.12 | FEB | 13.93
FEB | 25.31 | FEB | 9.69 | DEC | 31.08 | FEB | 12.38 | NOV | 29.18 | JUN | 11.68
JAN | 20.96 | DEC | 6.08 | NOV | 30.91 | DEC | 8.41 | DEC | 28.27 | JAN | 9.39
JUL | 17.54 | JAN | 5.70 | JUN | 26.78 | JAN | 7.17 | JUN | 25.01 | NOV | 9.33
JUN | 14.59 | NOV | 4.73 | FEB | 26.19 | NOV | 6.26 | FEB | 24.81 | DEC | 9.28
OCT | 11.94 | MAY | 2.00 | JAN | 22.26 | MAY | 3.11 | JAN | 21.55 | OCT | 8.42
MAY | 7.43 | OCT | 1.13 | MAY | 19.86 | OCT | 2.50 | MAY | 19.15 | MAY | 4.39
MAR | 6.10 | MAR | -7.40 | APR | 16.67 | MAR | -4.05 | APR | 16.26 | MAR | -1.06
APR | 4.40 | APR | -11.56 | MAR | 12.40 | APR | -8.59 | MAR | 12.23 | APR | -4.17

## Slide 51: Open Floor Q/A

## Slide 52: Thank you For Listening! Please Visit our Website
Visit the TransAlta official image library to access more photographic imagery to use in presentations
NOTE TO USER: THIS IS A PRE-BUILT SLIDE
Duplicate and update the information on this slide as needed and delete all yellow notes before using in final presentation.
OR: delete this slide if not being used in final presentation